## Slide 1: Hardware-Accelerated Convolutional Neural Networks on RISC-V Processor Integrated with FPGA
ACHUTHA ASWIN NAICK
2nd Year ECE
College of Engineering Trivandrum

## Slide 2: CONTENTS
Zynq 7000 Series FPGA Development Board (ZedBoard)
32-bit 5-stage pipelined RISC-V (RV32I) Processor in Verilog HDL
Custom AXI4 Stream IP generation
Implementation of Neural Networks in Verilog HDL
Integration of RISC-V processor and Neural Networks
Results
Next Task
Extras

## Slide 3: Zynq 7000 FPGA Development Board (ZedBoard)
(Source: Digilent Zynq 7000 ZedBoard datasheet)

## Slide 4: Why ZedBoard?
Zynq SoC: Dual-core ARM Cortex-A9 + Artix-7 FPGA ideal for HW/SW design
RISC-V on FPGA: Deploy pipelined RISC-V core in FPGA fabric for full control of dataflow and logic
AXI Interconnect: High-speed PS ↔ PL communication for data transfer and accelerator control
512MB DDR3 RAM: Shared memory for MNIST image data, model weights, biases and intermediate buffers
Neural Network Acceleration: FPGA used for CNN layers, ReLU, Sigmoid, fully connected layers using fixed-point representation logic
Toolchain Support: Works with Vivado, Vitis
Edge AI Ready: Compact, low-power system ideal for real-time digit classification in embedded settings

## Slide 5: Overview of ZedBoard
Dual Core ARM Cortex-A9 (Processing System (PS)) : Controls overall flow, loads MNIST image data, initiates classification
Artix-7 FPGA (Programmable Logic (PL)) : Implements RISC-V core + accelerates Neural Network computations
PS-PL Link : AXI Interconnect Interface; Moves image pixels from PS to PL, retrieves predictions

## Slide 6: Day-Wise Progress
6th June: Explored ZedBoard and studied its datasheet.
7th June: Implemented RISC-V Add and Immediate instructions.
8th June: Learned RISC-V ISA formats (R/I/S); designed 32-bit ALU.
9th June: Created ALU Decoder, Main Decoder, and memory/mux components.
10th June: Built pipeline registers, writeback mux, regfile, PC mux.
11th June: Completed datapath, controller, hazard unit; tested ZedBoard OLED.
12th June: Started Neural Networks; learned Perceptrons and bias.
13th June: Covered Sigmoid/ReLU concepts; intro to digit classification.
16th June: Explored activation functions; designed single neuron in Verilog.
17th June: Implemented ReLU/Sigmoid, designed NN layers, learned AXI/DMA.
18th June: Integrated NN with AXI/DMA; achieved 90–98% accuracy.
19th June: Created ZyNet IP and interfaced with Zynq PS via AXI.
20th June: Bitstream generated; hardware exported for final deployment.
23rd June: Started image processing; designed line buffer and MAC unit.
24th June: Implemented control logic for buffer/mux; handled pixel data.
25th June: Designed testbench for image processing logic.

## Slide 7: Section I: RISC-V Processor
32-bit RISC-V 5-stage pipelined Processor Implementation in Verilog HDL

## Slide 8: Why Choose RISC-V?
Modular and Scalable
  Supports base integer instructions (RV32I)
  Integration-friendly for hardware accelerators (e.g., MNIST classifier)
Optimized for Efficiency
  Simple, clean instruction set
Supported by a large, growing ecosystem of compilers and tools
Flexible for Both Software and Hardware Co-Design
  Facilitates tight integration between processor and custom IPs on FPGAs

## Slide 9
32-bit RISC-V Processor: Complete Diagram

## Slide 10: Modules Implemented in Verilog HDL
Components
Main Decoder
ALU
Memory
Data Memory
Instruction Memory
Immediate Extend
Forwarding Units (A , B)
Datapath Pipeline Registers
Controller Pipeline Registers
Supporting Modules
ALU Decoder
Program Counter MUX
Register File
IF/ID Register
ID/EX Register
EX/MEM Register
MEM/WB Register
ID/EX Register (CTRL)
EX/MEM Register (CTRL)
MEM/WB Register (CTRL)
Adder
2x1 MUX
4x1 MUX
Reset Flip-Flop
Write Back MUX
Integration
Controller
Datapath
Hazard Detection Unit
RISC-V Integrated
RISC-V top
Tool used: AMD Vivado 2023.2

## Slide 11: RISC-V RTL Design
Tool used: AMD Vivado 2023.2
RTL Analyzer

## Slide 12: Section II: Custom AXI-4 Stream IP
Custom AXI4 Stream IP Block Design generated for testing Inverting functionality

## Slide 13: Configuration of DMA Controller
Slower DMA controller
Faster DMA controller
(Drawback: one DMA Controller for one peripheral)

## Slide 14: Overview of DMA on Zynq
512MB DDR3: This will store image weights, biases

## Slide 15: AXI (Advanced eXtensible Interface) [Some Terminologies]
AXI:
  Memory mapped
  Full interface
  Has Bursting (bursting refers to a high-performance data transfer feature where multiple data words are transferred in one transaction rather than one at a time. This improves throughput and reduces latency and overhead.)
AXIS:
  Not Memory mapped
  Directly point to point interface between Master and Slave
AXI Lite:
  Memory mapped
  Simple and low throughput interface

## Slide 16: Overview of AXI Interface
Feature | AXI (Full) | AXI Lite | AXI Stream (AXIS)
Memory Mapped | ✅ Yes | ✅ Yes | ❌ No
Point-to-Point | ❌ No (via interconnect) | ❌ No | ✅ Yes (direct Master ↔ Slave)
Bursting Support | ✅ Yes | ❌ No (only single beat transfers) | ✅ Yes (continuous stream, no address)
Use Case | High-throughput data (DMA, memory) | Configuration, register access | Real-time streaming (video, sensors)
Complexity | High | Low | Medium

## Slide 17: Xilinx DMA IP (Xilinx AXI DMA)
S_AXI_LITE: interface for configuring DMA from processor (AXI4-Lite protocol)
S_AXIS_S2MM: read interface from peripheral to DMA (AXI Stream protocol)
M_AXI_MM2S: read interface from Memory to DMA (AXI4 Full protocol)
M_AXI_S2MM: write interface from DMA to Memory (AXI4 Full protocol)
M_AXIS_MM2S: write interface from DMA to peripheral (AXI Stream protocol)
***MM2S: Memory Mapped to Stream
***S2MM: Stream to Memory Mapped
(performance higher than AXI Lite)

## Slide 18: AXI-4 Stream IP Testing (Inverter)
DMA System level Design with AXI interface
Tool used: AMD Vivado 2023.2 IP Packager

## Slide 19: AXI-4 Stream IP Simulation Waveform (for an Inverter)
Tool used: AMD Vivado 2023.2
Simulation

## Slide 20: Section III: Neural Networks
Implementation of MNIST Dataset recognition using a fully connected Convolutional Neural Network

## Slide 21: Dataset
MNIST Dataset: Contains 28x28 grayscale images of handwritten digits (0–9).
Flattening: Each image is converted into a 784-length (28×28) 1D array of pixel values.
Normalization: Pixel intensities (0–255) are scaled to range [0, 1] or [-1, 1] for better learning.
Binary Conversion: Normalized values are quantized and represented in binary (fixed-point format) for FPGA compatibility.
Memory Storage: Binary pixel data is stored in FPGA memory (e.g., BRAM) for input to the CNN.
Efficiency: Preprocessing simplifies data transfer and speeds up inference on FPGA hardware.

## Slide 22: System Architecture

## Slide 23: CNN Network Design of a Single Neuron

## Slide 24: Layer Design
Parallel Input: All 784 input nodes send
data simultaneously via AXI interface.
Data Flattening: 28×28 image is reshaped into a 1D array to match neuron inputs.
Weight & Bias Multiplication: Each input
is multiplied with its weight and added to
bias.
Pipelined Architecture: Enables
overlapping of operations across layers
for high throughput.
Epoch-Based Execution: This process repeats throughout all training and testing epochs.
10

## Slide 25: Module Implemented in Verilog HDL
Layer
Layer 1
Layer 2
Layer 3
Layer 4
Memory Instantiation Functions
w_x_y
b_x_y
Sigmoid Content
Basic Structure
Neuron
Memory
AXI Lite Wrapper
Sigmoid ROM
Weight Memory
ReLU
Max Finder (Softmax)
ReLU Content

## Slide 26: Neural Networks (zynet) RTL Design
Tool used: AMD Vivado 2023.2
RTL Analyzer

## Slide 27: Neural Network Implementation Device Results

## Slide 28: Resource Utilization Data for different Functions
ReLU
Sigmoid Size 10 Sigmoid Size 5

## Slide 29: Training and Prediction Simulation Results
Above video supports for Sigmoid size 10
Epoch based training 10,000 test data

## Slide 30: Timing Results for different Functions
ReLU
Worst Negative Slack : -0.799
Fmax: 208MHz
Accuracy: 90.00000%
Sigmoid Size 10
  Worst Negative Slack : -0.717
  Fmax: 212MHz
  Accuracy: 98.00000%
*Sigmoid Size 5
  Worst Negative Slack : -0.816
  Fmax 207MHz
  Accuracy: 96.00000%
***Ideally considered: 250MHz

## Slide 31: Neural Network IP Block Design (zynet)
Tool used: AMD Vivado 2023.2 IP Packager

## Slide 32: Final Design Timing Summary for zynet IP Block System Design
Worst Negative Slack: 0.951ns
Fmax: 327MHz (higher than 250MHz (considered))

## Slide 33: Integration of RISC-V Processor and Neural Networks
Tool used: AMD Vivado 2023.2 IP Packager
***Currently under testing

## Slide 34: Probable Basic Design of system architecture
Most probable basic structure with type of interfaces

## Slide 35: Major Problems Encountered
Failure of AMD Vivado and Vitis softwares multiple times and eventually hanging up of these software in later stages.
Failure of Linux Operating System in later stages.
Availability of RISC-V GNU GCC Complier Toolchain only for Linux OS and not for Windows OS.

## Slide 36: Future Task
Try to deploy the whole system architecture on the Zynq 7000 series ZedBoard FPGA Development Board
Try interfacing VGA Controller with a display to manually input image pixel values using arrow keys of a system keyboard.

## Slide 37: Extras
Implement Image Processing of a grayscale image of size 512*512 using Verilog HDL initially to find out the edge detection of the input BMP grayscale image.
Test this Image Processing of the same image using Python programming language and deploy it on NVIDIA Jetson Nano board / Texas Instruments MCU CC2650.

## Slide 38: Thank You